## Slide 1: Digital Design
Prof. GSS Chalapathi,
Prof. Saurabh Gandhi,
Prof. Ramesh Sambangi

## Slide 2
Final expression after simplification with k-maps must include what terms?
While applying k-maps, don’t cares should be treated as?
Review questions

## Slide 3
A circuit to turn on the right LED
Turn on exactly 1 of 8 LEDs, depending on a certain stored value.
How many bits do we need to store the value of the LED to be turned on?
How many output wires does the circuit need to turn on the correct LED?
1
0
1
101₂ = 5
3-to-8
DECODER
◀ only this one is ON
LED0
LED1
LED2
LED3
LED4
LED5
LED6
LED7
A decoder expands a compact 3-bit code back into 8 individual output lines — exactly one active at a time.

## Slide 4
Decoders

## Slide 5
Building a decoder

## Slide 6
Building a decoder – the circuit

## Slide 7
Decoders can include an enable input (EN)
EN = 0 disables the decoder (all outputs are 0)
EN = 1 enables the decoder (exactly 1 output is 1 depending on the input)
Decoders with ‘enable’ inputs

## Slide 8
3 – to – 8 decoder

## Slide 9
Building a 3 - to - 8 decoder
Can you think of a ‘hierarchical’ design for this decoder, like we did with half and full adders?

## Slide 10
Hierarchical decoder design
Verify this circuit: use equations for the 2-to-4 decoder to derive equations for 3-to-8 decoder!

## Slide 11
Notice anything special about the 3-to-8 decoder output expressions?

## Slide 12
Example: building an adder with decoder(s)
Verify:
Reuse the same decoder for both outputs:
(Dis)advantages of this approach?

## Slide 13
Active-high and active-low decoders

## Slide 14
Active-low decoders are maxterm generators!

## Slide 15
Active-low decoder example

## Slide 16
Opposite function as that of a decoder
Takes 2n inputs, and generates the binary equivalent of the input rank as output
Encoders

## Slide 17
Two ambiguities associated with the design of the simple encoder shown previously:
It assumes only one input to be active. If two inputs are simultaneously active, output becomes invalid.
D0 = 1 or all Ds = 0 will both generate an output of 0
Encoder design issues
Solution: Priority encoders
Multiple asserted inputs allowed; one has priority over others
Separate indication of no-asserted-inputs

## Slide 18
Example: 4-to-2 priority encoder
If two or more inputs are simultaneously 1, output will correspond to the rank of the highest priority input
‘Valid’ output indicator, set to 1 only if at least one of the inputs is 1

## Slide 19
Use of binary encoder (example)

## Slide 20
Uses of priority encoders (example)